# Specific board support

Several readymade boards are supported out of the box. For each board, there is a corresponding C file that exposes the peripherals that are connected to that board. If the board has any external connection ports then these ports are also exposed though the board driver (although handling of devices connected to these ports is up to the application).

## Multiwii Flight Controller

Multiwii controller har following peripherals accessible through ”boards/flight_control/multiwii.c”:

- 4 supported pwm outputs (D3, D11, D5, D6)
- 4 pwm inputs (D2, D4, D7, D8)
- 6 gpio (analog in/digital out) (D9, D10, D12, A0, A1, A2)
- Accelerometer
- Gyroscope
- Magnetometer
- Barometer
- Temperature sensor
- 1 USART
- 1 I2C interface
- 1 Led

### Organization
Multiwii pins are designated on the board by the letters above. The hardware pins are mapped to the API pins as follows:
- PWM Output:
  - D6 - MWII_OUT_PWM0
  - D5 - MWII_OUT_PWM1
  - D11 - MWII_OUT_PWM2
  - D3 – MWII_OUT_PWM3
- PWM Capture:
  - D2 - MWII_IN_PWM0
  - D4 - MWII_IN_PWM1
  - D7 - MWII_IN_PWM2
  - D8 - MWII_IN_PWM3